GENERAL INSTRUCTIONS FOR

RABID MODELS 3D-PRINTED PARTS

Check your parts to check for any imperfections. Please note that it is normal for 3D-printed parts to have left-over flashing or supports which should be removed.  Most of our products have this material already removed for you.

Coarse sandpaper and a sharp hobby knife can quickly remove extra bits which you may find on the surface of the plastic.   Sand the parts using medium-grit sandpaper so that all imperfections are removed.  The plastic is quite hard – by using progressively finer grits a smooth surface can be achieved.

We suggest that you should paint the separate parts with a plastic primer and then a plastic-compatible spray-paint. Painting is necessary since UV rays can degrade the 3D-plastic material over time if its not protected. For a gloss coat finish, use a clear spray such as polyurethane or Beacon's “Hobby-Coat”.

Our 3D-printed aircraft tires are made from a flexible material called “TPU” (Thermoplastic PolyUrethane) which is relatively difficult to manufacture. The tires cannot be sanded. The wheel hubs are made from PETG and should not require much work since they are essentially flat.

To install the wheel hubs, first ensure that they fit the tire properly.  Check the tire “bead” to make sure there aren't any bits of plastic that prevent the hubs from sitting flush.  Use a flexible plastic-compatible cement such as Beacon's Foam-Tac, Fabri-Tac, or Hyperbond rubberized CA to glue the hubs onto the tire (one on each side) making sure that they are seated properly. Wheel hubs that have “spokes” should be lined up on both sides.  Remember to also glue the inside surface of the hubs (they will touch each other). Press firmly to ensure that the wheel hubs are flat and true.

You will notice that the wheel hubs have a “starter hole” - we purposely did not drill out the hole since its possible for the customer to use different size axles. Drill an appropriate hole for the axle, but take care:  drill the hole slowly (by hand) since the plastic will melt with a high-speed drill.  Drill each side separately.

Of course you can obtain spare or replacement parts from Rabid Models.

Thank you for your purchase!

WWW.RABIDMODELS.COM

email:  sales@rabidmodels.com